Switch between Memory Channel mode and VFO  (tuning) mode

Memory Channel mode has  ### upper left corner screen

Press [V/M] key to switch

VFO mode :

To  Enter Freq. - enter 000.000

For Memory Channel Mode :

Enter – ### then press [F/W]

In VFO, to Save Frequency

Press and hold [F/W] for 1 sec, ### start flashing

Rotate Knob to select  Memory channel,

Press [F/W] to save.

To Save a Frequency with a Tone

Save a Frequency as above

Then Press [F/W] then [1]

Rotate Knob and select <tone>

Press [PTT] to enter

Then press [F/W] then [2]

Rotate knob to select frequency

Press [F/W] to save

Press and hold [F/W] for 1 sec, ### start flashing

Rotate Knob to select  Memory channel,

Press [F/W] to save.

Enter a Different Transmit from Receive,

Save a Receive Frequency as above and

record the memory channel ###

In VFO mode, enter Transmit Freq., 000.000,

If tone needed, then Press [F/W] then [1]

Rotate knob and select <tone>

Press [PTT] to enter

Then press [F/W] then [2]

Rotate knob to select frequency

Press [F/W] to save

Press and Hold [F/W] for 1 sec.

Rotate knob to same memory channel ###

Press and Hold [PTT] ,

While still holding [PTT], Then press [F/W]

To Lock Radio

Press [F/W] then [6] to lock

Padlock will appear on screen when locked

Then press [F/W] then [6] to unlock

To Change Transmit Power

Press [F/W], then [3]

Then rotate knob to select power level

Press [PTT] to enter

Tone Scan

With frequency on screen,

Enable tone operation, Press [F/W] then [1]

Rotate Knob and select <tone>

Press [PTT] to enter

Press [F/W] then [2]

Press and hold  [▲MHz] or [▼MHz] to start scan

Press [F/W] to lock in tone

Press [F/W] to return

Banks (Memory Mode)

Press and hold [Band] for 1 sec.

Rotate Knob to Select 1 thru 10 or No Bank

Press [V/M]

Assign Memorized Freq to a Bank

Recall Memorized freq. To display

Press and hold [Band] for 1 sec.

Rotate Knob to Select Bank 1 thru 10

Press and hold [V/M] for 1 sec.

Remove Memorized Freq from Bank

Recall Memorized freq. To display

Press and hold [Band] for 1 sec.

Press [F/W]

Scanning Frequencies

Select in Bank or Memory or VFO

Press and hold  [▲MHz] or [▼MHz] for 1 sec

Will stop and hold during transmission

The decimal point will flash during scanning

Use [PTT] to terminate scan

It will not transmit until scanning is terminated

To Delete a Frequency

Press and hold  [F/W] for 1 sec– ###  start flashing

Rotate Knob to select  Memory location for deletion,

Press [HM/RV] to delete.

Ensure that “Wires” is off

If small nuclear symbol is in upper right corner of the display, Press [0] to switch off